## Slide 1
PHASE 1
BILL OF
MATERIALS
Meridian Bank
Wide Area Network Deployment
5-Site Capstone Network Architecture — CS 4122: Wide Area Networks
Prepared for: ICT University WAN Defense Board Course: ISN 3132 / CS 4122 — Wide Area Networks Milestone: Phase 1 — Physical Layer Bill of Materials
July 2026

## Slide 2
What This Deliverable Covers
Phase 1 Milestone — before a single configuration line is written
Router Selection
Exact model per site, sized to throughput & user count
WAN Transceivers
Transceiver type and quantity for every inter-site link
Fiber & Connectors
Fiber type (SMF/MMF) and connector standard (LC)
Copper & Pinouts
V.35 and RS-232 cabling with DTE/DCE pin mapping
Clocking Plan
DCE/DTE assignment and required clock rate per link
Budget Compliance
Full itemized cost, held under the $15,000 ceiling
Meridian Bank WAN Deployment | CS 4122 Capstone | Phase 1: Bill of Materials
2

## Slide 3
Project Recap — The Meridian Bank Scenario
5 sites across Cameroon, one non-negotiable set of constraints
Site | Users | Role | Distance from HQ
HQ — Yaoundé | 500 | Core banking servers, 99.999% uptime target | —
Branch A — Douala | 120 | Major commercial hub | 200 km
Branch B — Buea | 60 | Regional office | 300 km
Branch C — Garoua | 30 | Northern gateway | 800 km
Branch D — Maroua | 15 | Remote presence | 1,000 km
Site | Users | Role | Distance from HQ
Non-Negotiable Constraints
10 Mbps minimum throughput to every branch
$15,000 total hardware budget — strict ceiling
Layer 2 CHAP authentication on all inter-branch traffic
1,000 km longest single link — HQ to Maroua
Meridian Bank WAN Deployment | CS 4122 Capstone | Phase 1: Bill of Materials
3

## Slide 4
Design Philosophy — Respect the Physics of the Link
Why this BoM is not "just pick the fastest SFP"
The trap: Standard fiber transceivers are reach-limited — SX ≈ 550 m, LX ≈ 10 km, ZX ≈ 70–80 km. Not one of them reaches the 200–1,000 km spans between HQ and the branches. A BoM that simply specifies "SFP" for every link fails on Day 1.
The fix: The bank does not build its own 1,000 km fiber run. Camtel, the carrier, already owns that long-haul path (with its own amplification and regeneration). Meridian Bank's Bill of Materials only needs to cover the local loop — the short hop from the router to the carrier's demarcation point in each city. That is a design decision, and it is the one this BoM makes.
Physical layer first
If Layer 1 is broken, Layers 2 and 3 never get a chance to matter.
Carrier carries the distance
Local loop optics only; Camtel's backbone carries the km.
Resilience by design
Every site gets a primary fiber path and a serial backup path.
Meridian Bank WAN Deployment | CS 4122 Capstone | Phase 1: Bill of Materials
4

## Slide 5
Target Topology — Dual-Path Hub and Spoke
Every branch reaches HQ through the Camtel core, on two independent paths
HQ
Yaoundé
Camtel MPLS / Metro-E Core
Douala
200 km
Buea
300 km
Garoua
800 km
Maroua
1,000 km
Primary — Camtel Metro-Ethernet / MPLS (fiber, SFP-LX)
Backup — E1 leased line via CSU/DSU (V.35 serial)
Meridian Bank WAN Deployment | CS 4122 Capstone | Phase 1: Bill of Materials
5

## Slide 6
Router Selection
Sized to user count, throughput demand, and role — not one-size-fits-all
Site | Users | Model | WAN Interfaces | Unit Cost
HQ — Yaoundé | 500 | Cisco ISR 4331 | 2× GE (fiber) + 4× Serial NIM (E1 backup) | $2,450
Douala | 120 | Cisco ISR 1121-4P | 1× GE (fiber) + 1× Serial (E1 backup) | $950
Buea | 60 | Cisco ISR 1101-4P | 1× GE (fiber) + 1× Serial (E1 backup) | $700
Garoua | 30 | Cisco ISR 1101 | 1× GE (fiber) + 1× Serial (E1 backup) | $550
Maroua | 15 | Cisco ISR 1101 | 1× GE (fiber) + 1× Serial (E1 backup) | $550
Site | Users | Model | WAN Interfaces | Unit Cost
Justification: The ISR 4331 gives HQ headroom for 500 users, 99.999%-uptime routing, and enough NIM slots to aggregate four backup serial links. Branch routers scale down with user count — the ISR 1101 series covers Garoua and Maroua's light 15–30 user load at a fraction of the cost, protecting the budget for the larger branches.
Meridian Bank WAN Deployment | CS 4122 Capstone | Phase 1: Bill of Materials
6

## Slide 7
Primary WAN Link — Fiber to the Carrier Demarc
Every site's local loop, not the inter-city span, sets the optic reach
Site | Transceiver | Fiber Type | Connector | Local-Loop Reach Needed
HQ — Yaoundé | SFP-LX (1310 nm) | SMF, 9/125 µm | LC (duplex) | ≤ 10 km — within rating
Douala | SFP-LX (1310 nm) | SMF, 9/125 µm | LC (duplex) | ≤ 10 km — within rating
Buea | SFP-LX (1310 nm) | SMF, 9/125 µm | LC (duplex) | ≤ 10 km — within rating
Garoua | SFP-LX (1310 nm) | SMF, 9/125 µm | LC (duplex) | ≤ 10 km — within rating
Maroua | SFP-LX (1310 nm) | SMF, 9/125 µm | LC (duplex) | ≤ 10 km — within rating
Site | Transceiver | Fiber Type | Connector | Local-Loop Reach Needed
Why SMF + LX, and not MMF or a ZX/SX mismatch:
• Multimode SFPs are for short campus runs — ordering MMF for any carrier local loop risks a dead link on Day 1. • LX (single-mode, 10 km) comfortably covers every realistic local loop, whether the branch sits 200 km or 1,000 km from HQ — the long haul is Camtel's fiber, not the bank's. • Standardizing on one transceiver part number across all 5 sites simplifies sparing and lowers unit cost.
Meridian Bank WAN Deployment | CS 4122 Capstone | Phase 1: Bill of Materials
7

## Slide 8
Backup WAN Link — Serial E1 via CSU/DSU
Resilience for the 99.999%-uptime requirement, with full clocking spec
Site | Circuit | Interface Device | Cable | DCE / DTE | Clock Rate
HQ | E1 (2.048 Mbps) | External CSU/DSU | V.35 (DTE) | CSU/DSU = DCE Router = DTE | 2,048,000 bps
Douala | E1 (2.048 Mbps) | External CSU/DSU | V.35 (DTE) | CSU/DSU = DCE Router = DTE | 2,048,000 bps
Buea | E1 (2.048 Mbps) | External CSU/DSU | V.35 (DTE) | CSU/DSU = DCE Router = DTE | 2,048,000 bps
Garoua | E1 (2.048 Mbps) | External CSU/DSU | V.35 (DTE) | CSU/DSU = DCE Router = DTE | 2,048,000 bps
Maroua | E1 (2.048 Mbps) | External CSU/DSU | V.35 (DTE) | CSU/DSU = DCE Router = DTE | 2,048,000 bps
Site | Circuit | Interface Device | Cable | DCE / DTE | Clock Rate
Clocking Path
Router
(DTE — receives clock)
CSU/DSU
(DCE — provides clock)
Camtel E1 Demarc
Rule: the DCE (CSU/DSU) always supplies clocking. A clock-rate mismatch here is the #1 cause of a serial link stuck in "down/down."
Meridian Bank WAN Deployment | CS 4122 Capstone | Phase 1: Bill of Materials
8

## Slide 9
Console & Management Cabling
RS-232 remains the most reliable path in when the network itself is down
Component | Standard | Connector | Setting / Notes
Console cable (×5, one per router) | RS-232 (rollover) | RJ-45 → DB-9 adapter | 9600-8-N-1, no flow control
Router LAN uplinks (×5) | Ethernet, T568B | RJ-45 (straight-through) | Router GE port → access switch
Patch panel jumpers | Cat6, T568B | RJ-45 (straight-through) | Demarc patch panel → router
Component | Standard | Connector | Setting / Notes
Why every cable type still gets a line item:
• A crossover cable where straight-through is required produces a link that is physically "up" but passes no traffic — a classic Layer 1 trap this BoM avoids by specifying pinout, not just "a cable."
• No documented DTE/DCE assignment a technician on-site who guesses wrong will spend hours chasing a clock-rate mismatch that a labeled BoM prevents in five minutes.
• Skipping the console cable removes the only path into a router once a misconfiguration takes down its network interfaces.
Meridian Bank WAN Deployment | CS 4122 Capstone | Phase 1: Bill of Materials
9

## Slide 10
Full Itemized Bill of Materials
5 sites, primary + backup paths, fully priced
Item | Qty | Unit Cost | Line Total
Cisco ISR 4331 (HQ router) | 1 | $2,450 | $2,450
Cisco ISR 1121-4P (Douala router) | 1 | $950 | $950
Cisco ISR 1101-4P (Buea router) | 1 | $700 | $700
Cisco ISR 1101 (Garoua & Maroua routers) | 2 | $550 | $1,100
SFP-LX transceiver, 1310 nm, SMF | 5 | $120 | $600
SMF patch cable, LC-LC duplex | 5 | $15 | $75
External CSU/DSU unit | 5 | $180 | $900
V.35 serial cable (DTE, router-side) | 5 | $45 | $225
E1 demarc cable, RJ-48C (carrier-side) | 5 | $20 | $100
RS-232 rollover console cable | 5 | $15 | $75
Rack accessories & patch panel hardware | 1 lot | $150 | $150
Item | Qty | Unit Cost | Line Total
BUDGET SUMMARY
$7,325
Total Phase 1 Spend
$15,000
Approved Ceiling
49% utilized
$7,675 reserved for Phase 2 — firewalls, LAN switching, and ACL/NAT licensing.
Meridian Bank WAN Deployment | CS 4122 Capstone | Phase 1: Bill of Materials
10

## Slide 11
Budget Allocation by Category
Where the $7,325 goes — and what headroom remains
Chart: 
| Routers | Fiber & SFP | CSU/DSU | Serial/Console Cables | Rack & Misc | Unused Headroom
Cost ($) | 5200 | 675 | 900 | 400 | 150 | 7675
Meridian Bank WAN Deployment | CS 4122 Capstone | Phase 1: Bill of Materials
11

## Slide 12
What This BoM Protects Against
Physical-layer mistakes are the most expensive to fix — hardware is already shipped across the country
Wrong fiber mode
MMF ordered for a carrier hand-off: dead link on Day 1, full reship cycle to fix.
Missing clock rate
No clock rate on the DCE side: serial interface stays down/down indefinitely.
No console access
No RS-232 cable on-site: a misconfigured router becomes unreachable remotely.
Single path only
One WAN link per branch: any fiber cut takes the branch fully offline.
Undocumented pinout
Crossover swapped for straight-through: link shows "up" but never passes traffic.
Budget overrun
Untracked spend: exceeding $15,000 stops procurement mid-deployment.
Meridian Bank WAN Deployment | CS 4122 Capstone | Phase 1: Bill of Materials
12

## Slide 13
Phase 1 Sign-Off & What Comes Next
Once hardware is ordered and validated, the logical build begins
1
Procure & Ship
Order all Phase 1 line items against the $7,325 spend, within the $15,000 ceiling.
2
Physical Install & Validate
Rack equipment, run fiber and serial cabling, confirm loopback and link-light status per site.
3
Phase 2 — Logical Build
Configure PPP with CHAP, VLSM /30 addressing, and OSPF for automatic failover across all five sites.
4
Phase 3 — Capstone Defence
3-hour build-off, instructor-injected fault gauntlet, and Board of Directors architecture defence.
"Ask questions anytime — participation is encouraged."
Meridian Bank WAN Deployment | CS 4122 Capstone | Phase 1: Bill of Materials
13